## Slide 1: The NEOSSat Experience: 5 Years in the Life of Canada’s Space Surveillance Telescope
Viqar Abbasi (CSA)
STEFAN THORSTEINSON (DRDC)
David Balam (SpaceGuard)
Jason ROWE (BISHOP’s UNIVERSITY)
LAUCHIE R. SCOTT (DRDC)
DENIS LAURIN (CSA)
Michel Doyon (CSA)

## Slide 2: Canada’s space-based SSA sensors
SAPPHIRE: (Canada’s DND)
NEOSSat: (CSA & DRDC)
Launched 25 February 2013
PSLV C-20
Credit: ISRO

## Slide 3: Canada’s space-based SSA sensors
NEOSSat: (CSA & DRDC)
NEO+SSA R&D via microsatellite
SAPPHIRE: (Canada’s DND)
Part of US Space Surveillance Network (SSN)

## Slide 4: Near-Earth Object Surveillance Satellite NEOSSat
HEOSS (DND-DRDC)
Discovery, tracking and study of asteroids, especially interior to Earth orbit, comets and other astronomical objects
NESS (CSA)
Near Earth Space Surveillance  NESS
High Earth Orbit Space Surveillance  HEOSS
Demonstrate military utility of microsatellite platform
Gather metric observations of resident space objects in support of space situational awareness R&D

## Slide 5: NEOSSat Architecture
Architecture:
780 km Dawn-Dusk Sun-Synchronous Orbit
75kg microsatellite based on successful MOST space telescope
  15-cm aperture telescope, with 0.8⁰ field-of-view, 3” / pixel
  Imagers: 1024 x 1024 E2V CCDs (star tracker and science)
Low-cost microsatellite with minimal redundancy
3-axis stabilization w/ pointing accuracy ~1 arcseconds
  Coarse Sun Sensor (CSS)
  Magnetometer (MAG)
  Custom narrow-field Star Tracker along payload boresight
  4 MW200 reaction wheels with integrated rate sensors
  3 torque rods for momentum dumping
  2 GPS receivers for orbit determination
Team:
Funded by CSA and DRDC
Built by Microsat Systems Canada Inc (MSCI) of Toronto, Canada
Operated by CSA and SED in multi-mission control centre

## Slide 6: NEOSSat Modes
Key Operational Modes:
“Fine Point”: aka “Star Stare” mode
  Fix on stars with satellite/asteroid motion appearing as streaks in images
  good for imaging astronomical targets
  “Fine Slew”: aka “Track Rate” mode
  track moving space objects by matching their speed (stars appear as streaks)
Support Modes:
“Coarse Point” with CSS and MAG to provide initial pointing for star tracker acquisition
  enables transition to “fine” modes
“Rate Slew” to quickly move target-to-target

## Slide 7: NEOSSat Data Pipeline
CSA NEOSSat Constraint Checker
CSA PLAN (Integrated Schedule)
Satellite Telecommand Uplink
Satellite Telemetry Downlink`
FITS Processor
CSA Data Management
FITS
Astronomy FITS Image on CSA Open Data portal
Science Schedule (SSC) Planning
SSC
HEOSS FITS Image to DRDC
FITS

## Slide 8: NEOSSat Operations Timeline
2013: Launch and Commissioning
  MOST: star tracker parameters uploaded on a per-target basis
  NEOSSat: Continuous all-sky acquisition (0.8 degrees FOV) star tracker
  Software updates needed to ensure rapid and robust all-sky acquisition
2014-2015: Early operations
  HEOSS: regular imaging of GEO & HEO targets + astrometry and photometry
  NESS: MPC observatory code C53 assigned after astrometry of NEAs, comets
2016: Anomalies & Recoveries
  Failure #1: Magnetometer  no coarse attitude determination; tumbling
  Failure #2: Torque Rod controller failure  No momentum desaturation
  Health & Safety prioritized; software updates to work around failures
    #1: GPS-based attitude sensor to replace failed magnetometer
    #2: New desaturation control mode that orients residual dipole to dump onboard momentum
2017-2019: Return to Operations

## Slide 9: Resident Space Object (Satellites & Debris) Space Surveillance with NEOSSat

## Slide 10: NEOSSat SSA mission – High Earth Orbit Space Surveillance (HEOSS)

## Slide 11: SSA Operations
NEOSSat Constraints
NEOSSat -Z solar panel is constrained Sunward to maintain power and thermal constraints
Instrument radiator (+Z) points (preferentially) toward deep space
NEOSSat is outside of the South Atlantic Anomaly
Line-of-Sight Constraints
45 degree solar exclusion (outside of eclipse)
Angular rate of the RSO relative to NEOSSat is < 90 arcseconds/second
Grazing angle of RSO above the Earth limb is greater than > 10 degrees
Constant angular velocity Fine Slews

## Slide 12: Geostationary tracking
Images processed with a matched filter (astrometry) and drift compensating stacking (RSO detection)
<3’’ RMS metric accuracy down to V~16

## Slide 13: LEO to LEO Imaging
Self conjuncting objects
Instantaneous LEO conjunctions
High angular rate tracking
Proximity operations

## Slide 14: Self conjunctions
Predictions from CSA’s Collision Risk Assessment & Mitigation System (CRAMS) and SOCRATES
Iridium-17

## Slide 15
NEOSSat observations of conjuncting objects
Spot2 – miss distance 2.2 km

## Slide 16: Cosmos-2251 DEB Characterization

## Slide 17: Fast conjunction assessment
Cosmos 2251 DEB (again)
Covariance improvement (six obs)
10 Aug 2018

## Slide 18: Fast conjunction assessment
Source | Right Ascension (HH MM SS.S) | Declination (DD MM SS.S)
TLE | 15 28 45.8 | -37 01 54.3
SP vector | 15 28 54.5 | -37 01 49.9
Updated orbit | 15 28 54.1 | -37 02 01.5
TCA from TLE:
Time (UTCG): 10 Aug 2018 23:32:50.147
Radial (km): -3.327
In-Track (km): 0.239
Cross-Track (km): 2.280
Range (km): 4.040
Actual TCA:
Time (UTCG): 10 Aug 2018 23:32:50.177
Radial (km): -3.261
In-Track (km): 0.275
Cross-Track (km): 2.555
Range (km): 4.152

## Slide 19: Medium range high value asset monitoring
6 Jul 2018 – 2 Sapphire conjunctions
17:26:15 UTC
20:47:05 UTC
ORBCOMM-35
ORBCOMM-34

## Slide 20: Shared orbit monitoring

## Slide 21: Shared orbit monitoring
Residual processing from TLE initialized orbit
Covariance improvement

## Slide 22: Proximity Operations
12 Jun 2018: NEOSSat and Sapphire have minimum separation

## Slide 23: Proximity Operations
Covariance improvement

## Slide 24: LEO to LEO imaging summary
Future directions:
Improve conjunction warnings for LEO&GEO (fast POC re-assessment)
Integration with CRAMS
LEO constellation monitoring
Re-entry imaging attempts
Summary:
LEO optical SSA possible from an orbiting platform
Self conjuncting objects – Protect yourself!
Instantaneous LEO conjunctions – Keep fingers crossed
High angular rate tracking – Long period medium range monitoring
Proximity operations – In situ tracking

## Slide 25: Near Earth Object Surveillance with NEOSSat

## Slide 26: Asteroid Tracking with NEOSSat
Asteroid 1989VB, July 29, 2017
Asteroid 2012 TC4, Oct 12, 2017
Asteroid 2017 VR12, March 7, 2018
Advantages on NEOSSat:
No day-night or weather restrictions (just avoid imaging in South Atlantic Anomaly)
Highly stable platform with star-stare and track-rate modes
Direct measurement of parallax
Low solar elongation observations

## Slide 27: NEO Astrometry with NEOSSat
Stack of 5 images from 2017-VR12
Imaged 25 hrs through Earth approach
Process:
Dark, bias, dither/flat-field correction
Applying U. Victoria NEO astrometric software suite to NEOSSat data
  Shift-and-stack & keyhole
Submitting ADES format to MPC
Results:
Publication of C53 metrics on MPC
Limiting magnitude V~18 typically; ideal conditions V~19 achieved
Astrometric solution residuals in the range of 0.15”-0.35”
Next Steps:
Handle parallax in astrometry suite
Integrate automated astrometry into the data pipeline
Optimize survey strategy

## Slide 28: Comet and near-Earth asteroid observations and astrometry
Comet 249P imaged at 34⁰ solar elongation
Stack of 11 NEOSSat images, co-added at sidereal rate showing the tracklet of near-Earth asteroid 2002 AJ129

## Slide 29: Lower Solar Elongation at Eclipse
Field distribution of 213 low solar-elongation survey images, obtained over a 72-hour period (UT 2018 Dec. 22-24) and re-sampled onto an ecliptic (8⁰ x 5⁰) projection. The south-western field is 13.8⁰ from the sun
Nominal survey: 45-55⁰ solar elongation
Eclipse (Earth as a baffle): <15⁰ S.E.

## Slide 30: Parallax observations
Comet 46P campaign: Oct-Dec 2018 (Close Approach Dec 16th, 2018)
Comet Wirtanen (46P) as seen on UT 2018 Dec. 02 at 0.116 AU. Stack of 70 images obtained through 1/3 of NEOSSat’s orbital period, showing the effect of parallax. The geocentric motion vector was 261 arcseconds per hour at position angle 26.5⁰.

## Slide 31: New Applications with NEOSSat & Conclusions

## Slide 32: Exoplanet Transit Photometry
Process:
MOST & Kepler mission software suite applied to NEOSSat data
New image cleaning & photometry software for NEOSSat data
Follow-up on TESS and Spitzer candidate discoveries
Results:
Milli-magnitude photometric accuracy, easily capable to detect exoplanet transits
  Applicable to NEO & SSA
Next Steps:
Integrate new image cleaning & photometry into CSA data pipeline
WASP-33
TESS TOI-165
TVLM513-46
(Brown Dwarf/Spitzer)

## Slide 33: Astronomical demonstrations
Lagoon Nebula: Jun 30, 2017
Trifid Nebula: Jun 24, 2017
Eagle Nebula: July 14, 2017

## Slide 34: Conclusions
Demonstrated microsatellite platform can deliver advanced Space Situational Awareness (SSA) and NEO support
  Able to perform low solar elongation imaging not possible by ground
  Applicable in GEO & LEO regimes and in pre-conjunction situations
Technology Demonstration:
  Validated both astrometry and photometry with external partners
  Innovative control system with high-performance star tracker, reaction wheels & baffle, providing stability, flexibility and resilience
Future Work:
  Optimize planning for desired targets
  Fast/interrupt tasking support
  Processed data automation
  Exploit synergies

## Slide 35: Synergies: NEO & SSA
Single frame showing 2017-VR12 (boxed), with GEO satellites as large streaks
Single frame from low solar elongation survey image, with rotating satellite
Ground & Space sensors
Risk Assessment & Mitigation
Image Processing, Cloud, Big Data, AI…
Communications & Outreach

## Slide 36: Thank you!